## Slide 1
Summary (Q4)
Thu Ta Zaw
2415121095
  Optical Properties of Bone Tissue Phantom

## Slide 2
  Optical properties describe how a material interacts with light (electromagnetic radiation), especially UV, visible, and infrared regions.
  It can determine the color, transparency and reflectivity, which are essential for cells, sensors and lenses.
  When light interact with materials, it can be reflected, absorbed, transmitted, scattered and refracted.
  Optical Properties of Materials

## Slide 3
  Optical Properties of Materials
  Reflection
  Fraction of incident light reflected from a surface.
  Depends on surface roughness and refractive index.
  Important for mirrors and metallic surfaces.
Fig. Light reflection on surface
  Refraction
  Bending of light at the interface of two media.
  Governed by Snell’s Law.
  Important for lenses, optical fibers and skin.
Fig. Light refracted through the medium

## Slide 4
  Optical Properties of Materials
  Light Absorption
  Ability of material to absorb light energy.
  Related to electronic and vibrational transitions.
  Determines opacity and band gap behavior.
Fig. Light absorption phenomenon
  Light Scattering and Transmission
  Scattering is the redirection of light due to particles or defects.
  Transmission is the fraction of light that passes through a material.
Fig. Light Scattering and Transmission

## Slide 5
  Optical properties of samples (skins and phantom)
  The flowing data biomedical samples can be measured using the integrating spheres:
    Diffuse reflectance Rd, which is a fraction of light diffusely reflected from sample.
    Total transmittance Tt, which is a fraction of light transmitted (diffuse and direct).
    Specular reflectance Rs, which is a mirror-like surface reflection.
    Absorptance, which is a fraction of light absorbed by sample.
  The flowing optical properties can be calculated from the measured data:
    Absorption coefficient μa​, which describes the photon loss due to chromophore absorption.
    Reduced scattering μs′​, which describes diffusion strength of scattered light.
    Anisotropy Factor g, which describes the directionality of scattering (0 = isotropic and 1 = forward).
    Refractive index n, which describes the boundary reflection and transmission.
    Albedo a′, which describes the ratio of scattering to total extinction.
    Penetration depth δ, which describes the effective photon travel depth.

## Slide 6
  Integrating sphere is an optical measurement tool used to quantify how light interacts with scattering and absorbing media.
  It is a hollow spherical cavity, coated internally with a diffuse reflective material.
  The radiation introduced into an integrating sphere strikes the reflective walls and undergoes multiple diffuse reflections.
  After numerous reflections, the radiation is dispersed highly at the sphere walls.
  The resulting integrated radiation level is directly proportional to the initial level and may be easily measured by using a detector.
  Integrating Sphere
  Fig. Integrating sphere setup to measure the optical properties of sample

## Slide 7
  Integrating Sphere measurement (Reflectance)
Fig. Configurations necessary to make the measurements required for the calculation of
Notes: 𝑟_𝑠𝑡𝑑

## Slide 8
  Integrating Sphere measurement (Transmittance)
Fig. Configurations necessary to make the measurements required for the calculation of
Notes: 𝑟_𝑠𝑡𝑑

## Slide 9
  Integrating Sphere measurement (Transmittance)
Fig. Configurations necessary to make the measurements required for the calculation of
Notes: 𝑟_𝑠𝑡𝑑

## Slide 10
  Radiative Transport equation
  General Form
    radiance
    = absorption coefficient
    = scattering coefficient
    = phase function (Henyey-Greenstein)
    g = anisotropy (average cosine of scattering angle)
  Fig. Light propagation through the space
Notes: Time rate of change
Loss due to streaming
Loss due to interaction
Gain through scattering
Gain from sources

## Slide 11
  IAD Simulation
  Inverse Adding-Doubling (IAD) is a numerical method used to determine the intrinsic optical properties of turbid media such as:
    Absorption coefficient (μₐ)
    Scattering coefficient (μₛ)
    Anisotropy factor (g)
  From experimental measurements (integrating sphere), the following values are obtained:
    Total diffuse reflectance (Rₜ)
    Total diffuse transmittance (Tₜ)
    Un-scattered / collimated transmittance (Tc)
  Inverse Adding Doubling Method

## Slide 12
  Working Principle
  IAD works by repeatedly simulating light propagation and adjusting optical parameters until simulation matches measurement.
  IAD uses an iterative, trial-an-error approach to solve the radiative transport equation.
  The optical properties calculated from the algorithm are compared with measured value until they are in agree.
  Inverse Adding Doubling Method
  Fig. Process Diagram of IAD

## Slide 13
  Upcoming Plan
Set up Optical Sphere Experiment
Calibrate the measurement system with standard white
Create the Skin Phantom samples
Perform the measurement
Calculate the Optical properties of the skin phantom with IAD simulation
Calculate the Optical properties of the skin phantom with Monte Carlo simulation
Compare the two simulations result for the validation

## Slide 14
  Progress of Simulation
  Vid. Crimping of stent to deployment diameter

## Slide 15
  Error in simulations
  Poor-quality or distorted elements are not detected.
  Asymmetric contact pairs make load transfer and stiffness become inconsistent, causing convergence instability.
  Functional failure in contact pairs due to initial gaps between strut wires.
  There exit a severe modelling error, with over-complex contact definition, poor contact geometry preparation and unsafe default contact parameters.
  Progress of Simulation
  Fig. Non-convergence solution of the stent

## Slide 16
The End
THANK YOU FOR LISTENING
Thu Ta Zaw
2415121095